YU1QT  OBLONG  13el  144.200 MHz

R

A

D1

D2

h

S

S1

S2

etc...

AL wire 4mm

L R

826

h= 296                          Reflector

POSITION ON BOOM   0.0

LA

753

296                            Driver

POSITION ON BOOM  0.35

368.5                 (swr adjust tail)   20mm

16

L 1

704

296                          Director 1

POSITION ON BOOM   0.84

L 2

680

296                          Director 2

POSITION ON BOOM   1.62

L 3

650

296                          Director 3

POSITION ON BOOM   2.45

L 4

646

296                          Director 4

POSITION ON BOOM   3.37

L 5

632

296                          Director 5

POSITION ON BOOM   4.24

L 6

626

296                          Director 6

POSITION ON BOOM   5.2

L 7

628

296                          Director 7

POSITION ON BOOM   6.09

L 8

620

296                          Director 8

POSITION ON BOOM   7.03

L 9

626

296                          Director 9

POSITION ON BOOM   7.87

L 10

600

296                          Director 10

POSITION ON BOOM   8.87

L 11

628

296                          Director 11

POSITION ON BOOM   9.57

h    = 296mm

LR  =826

LA  =753

L1  =704

L2  =680

L3  =650

L4  =646

L5  =632

L6  =626

L7  =628

L8  =620

L9  =626

L10=600

L11=628

element position on boom

reflector =  0

S    =      350

S1  =      840

S2  =   1.620

S3  =   2.450

S4  =   3.370

S5  =   4.240

S6  =   5.200

S7  =   6.090

S8  =   7.030

S9  =   7.870

S10=   8.870

S11=   9.570mm