YU1QT  OBLONG  14el  144.200 MHz

R

A

D1

D2

h

S

S1

S2

etc...

AL wire 4mm

L R

826

h= 296                          Reflector

POSITION ON BOOM   0.0

LA

758

296                            Driver

POSITION ON BOOM  0.37

371                     (swr adjust tail)   20mm

16

L 1

706

296                          Director 1

POSITION ON BOOM   0.82

L 2

680

296                          Director 2

POSITION ON BOOM   1.61

L 3

649

296                          Director 3

POSITION ON BOOM   2.46

L 4

644

296                          Director 4

POSITION ON BOOM   3.38

L 5

631

296                          Director 5

POSITION ON BOOM   4.25

L 6

625

296                          Director 6

POSITION ON BOOM   5.19

L 7

628

296                          Director 7

POSITION ON BOOM   6.11

L 8

620

296                          Director 8

POSITION ON BOOM   7.04

L 9

627

296                          Director 9

POSITION ON BOOM   7.91

L 10

600

296                          Director 10

POSITION ON BOOM   8.85

L 11

627

296                          Director 11

POSITION ON BOOM   9.79

L 12

625

296                          Director 12

POSITION ON BOOM  10.45

h    = 296mm

LR  =826

LA  =758

L1  =706

L2  =680

L3  =649

L4  =644

L5  =631

L6  =625

L7  =628

L8  =620

L9  =627

L10=600

L11=627

L12=625

element position on boom

reflector =  0

S    =      370

S1  =      820

S2  =   1.610

S3  =   2.460

S4  =   3.380

S5  =   4.250

S6  =   5.190

S7  =   6.110

S8  =   7.040

S9  =   7.910

S10=   8.850

S11=   9.790

S12= 10.450mm