YU1QT  OBLONG  15el  144.200 MHz

R

A

D1

D2

h

S

S1

S2

etc...

AL wire 4mm

L R

822

h= 292                          Reflector

POSITION ON BOOM   0.0

LA

754

292                            Driver

POSITION ON BOOM  0.34

369                     (swr adjust tail)   20mm

16

L 1

702

292                          Director 1

POSITION ON BOOM   0.84

L 2

680

292                          Director 2

POSITION ON BOOM   1.62

L 3

651

292                          Director 3

POSITION ON BOOM   2.45

L 4

646

292                          Director 4

POSITION ON BOOM   3.37

L 5

632

292                          Director 5

POSITION ON BOOM   4.24

L 6

626

292                          Director 6

POSITION ON BOOM   5.2

L 7

628

292                          Director 7

POSITION ON BOOM   6.09

L 8

620

292                          Director 8

POSITION ON BOOM   7.04

L 9

626

292                          Director 9

POSITION ON BOOM   7.88

L 10

600

292                          Director 10

POSITION ON BOOM   8.88

L 11

628

292                          Director 11

POSITION ON BOOM   9.8

L 12

626

292                          Director 12

POSITION ON BOOM  10.67

L 13

625

292                          Director 13

POSITION ON BOOM  11.36

h    = 292mm

LR  =822

LA  =754

L1  =702

L2  =680

L3  =651

L4  =646

L5  =632

L6  =626

L7  =628

L8  =620

L9  =626

L10=600

L11=628

L12=626

L13=625

element position on boom

reflector =  0

S    =      330

S1  =      840

S2  =   1.620

S3  =   2.450

S4  =   3.370

S5  =   4.240

S6  =   5.200

S7  =   6.090

S8  =   7.040

S9  =   7.880

S10=   8.880

S11=   9.800

S12= 10.670

S13= 11.360mm