YU1QT  OBLONG 9el  144.200 MHz

R

A

D1

D2

h

S

S1

S2

etc...

AL wire 4mm

L R

860

h= 270                          Reflector

POSITION ON BOOM   0.0

LA

762

270                            Driver

POSITION ON BOOM  0.37

373                 (swr adjust tail)   20mm

16

L 1

724

270                          Director 1

POSITION ON BOOM   0.91

L 2

700

270                          Director 2

POSITION ON BOOM   1.67

L 3

673

270                          Director 3

POSITION ON BOOM   2.48

L 4

656

270                          Director 4

POSITION ON BOOM   3.4

L 5

655

270                          Director 5

POSITION ON BOOM   4.27

L 6

617

270                          Director 6

POSITION ON BOOM   5.13

L 7

620

270                          Director 7

POSITION ON BOOM   5.94

h    = 270mm

LR  =860

LA  =762

L1  =724

L2  =700

L3  =673

L4  =656

L5  =655

L6  =617

L7  =620

element position on boom

reflector =  0

S    =      370

S1  =      910

S2  =   1.670

S3  =   2.480

S4  =   3.400

S5  =   4.270

S6  =   5.130

S7  =   5.940mm