YU1QT  OBLONG II 10el  144.200 MHz

R

A

D1

D2

h

S

S1

S2

etc...

AL wire 4mm

L R

840

h= 282                          Reflector

POSITION ON BOOM   0.0

LA

760

282                            Driver

POSITION ON BOOM  0.35

372                 (swr adjust tail)   20mm

16

L 1

708

282                          Director 1

POSITION ON BOOM   0.8

L 2

694

282                          Director 2

POSITION ON BOOM   1.66

L 3

672

282                          Director 3

POSITION ON BOOM   2.5

L 4

654

282                          Director 4

POSITION ON BOOM   3.33

L 5

658

282                          Director 5

POSITION ON BOOM   4.25

L 6

620

282                          Director 6

POSITION ON BOOM   5.16

L 7

618

282                          Director 7

POSITION ON BOOM   5.99

L 8

614

282                          Director 8

POSITION ON BOOM   6.85

h    = 282mm

LR  =840

LA  =760

L1  =708

L2  =694

L3  =672

L4  =654

L5  =658

L6  =620

L7  =618

L8  =614

element position on boom

reflector =  0

S    =      350

S1  =      800

S2  =   1.660

S3  =   2.500

S4  =   3.330

S5  =   4.250

S6  =   5.160

S7  =   5.990

S8  =   6.850mm