YU1QT  OBLONG II 19el  144.200 MHz

R

A

D1

D2

h

S

S1

S2

etc...

AL wire 4mm

L R

832

h= 290                          Reflector

POSITION ON BOOM   0.0

LA

757

290                            Driver

POSITION ON BOOM  0.34

370,5                 (swr adjust tail)   20mm

16

L 1

714

290                          Director 1

POSITION ON BOOM   0.84

L 2

694

290                          Director 2

POSITION ON BOOM   1.55

L 3

656

290                          Director 3

POSITION ON BOOM   2.39

L 4

636

290                          Director 4

POSITION ON BOOM   3.28

L 5

628

290                          Director 5

POSITION ON BOOM   4.18

L 6

612

290                          Director 6

POSITION ON BOOM   5.11

L 7

608

290                          Director 7

POSITION ON BOOM   6.06

L 8

604

290                          Director 8

POSITION ON BOOM   7.0

L 9

602

290                          Director 9

POSITION ON BOOM   7.91

L 10

598

290                          Director 10

POSITION ON BOOM   8.87

L 11

612

290                          Director 11

POSITION ON BOOM   9.83

L 12

632

290                          Director 12

POSITION ON BOOM  10.7

L 13

584

290                          Director 13

POSITION ON BOOM  11.52

L 14

624

290                          Director 14

POSITION ON BOOM  12.71

L 15

622

290                          Director 15

POSITION ON BOOM  13.41

L 16

628

290                          Director 16

POSITION ON BOOM  14.39

L 17

608

290                          Director 17

POSITION ON BOOM  15.05

h    = 290mm

LR  =832

LA  =757

L1  =714

L2  =694

L3  =656

L4  =636

L5  =628

L6  =612

L7  =608

L8  =604

L9  =602

L10=598

L11=612

L12=632

L13=584

L14=624

L15=622

L16=628

L17=608

element position on boom

reflector =  0

S    =      340

S1  =      840

S2  =   1.550

S3  =   2.390

S4  =   3.280

S5  =   4.180

S6  =   5.110

S7  =   6.060

S8  =   7.000

S9  =   7.910

S10=   8.870

S11=   9.830

S12= 10.700

S13= 11.520

S14= 12.710

S15= 11.410

S16= 14.390

S17= 15.050mm